## Slide 1
LHCb Electronics Brainstorm

## Slide 2
Summary of ROUGH link estimate from sub-dets
 | Non zero-supp NZS | Zero supp ZS
Subdet | # GBT @ 3.2 Gbit/s | # GBT @ 3.2 Gbit/s
Velo | 8652 | 1176
ST | 31200 | 1200
OT | 6500 | 3500
RICH | 6292 | 1736
Calo | 1920 | 750
Muon | - | -
Total | 54,564 | 8,362
Assuming “300 CHF per link” |  | 
Cost CHF | 16.5 MCHF | 2.5 MCHF
Rough estimate for optical links in existing LHCb = 1.1 MCHF

## Slide 3
Architecture with ZS
hardware
trigger
Trigger
superviser
Data
HLT++
hardware
trigger
Trigger
superviser
Data
HLT++

## Slide 4
FE derandomising buffer
Absorb statistical fluctuations in data
Needs careful monitoring
Needs careful simulation
BE input buffer
Length = trigger latency
+ margin for derandomiser
BE trigger buffer
Small, re-ordering?
BE output buffer
Depends on output protocol
eg MEP factor?
Buffering with ZS
Triggering = BX correspondence

## Slide 5
Data Structure from front-end
Define maximum
lag between Bx and
transmission time.
if exceeded,
start truncating

## Slide 6
Modularity – something to think about . . . .
Example:

## Slide 7
Thoughts & Discussion
Clear cost saving in links by zero-suppressing in the front-ends
-----------------------------------------------------------------------------------
Need to implement front-end buffers after ZS
- carefully monitor event size and time lag
Event-sizes & statistical fluctuations have to be well understood
Additional bandwidth overhead with ZS on front-end
- transmit BX (12 bits?)
- transmit buffer status
Programmable devices would be very useful ! ! !
-----------------------------------------------------------------------------------
Interaction trigger/throttle decisions based on BX-ID tags
TELL40: buffer management + DAQ formatting
-----------------------------------------------------------------------------------
Existing Muon system is non-ZS: plan was to use this system
Front-end
Back-end